Admin command proposal draft: set host doorbell/eventidx memory

All referenced figures and sections indexes refers to the NVMe specification Revision 1.2a, October 23, 2015. Changes withing an existing Figure between the original content and the modification are indicated in blue color.

Proposal modifications:

* Add admin command in Figure 40 as shown below

Figure 40: Opcodes for Admin Commands
Opcode field			Combined opcode2	O/M1	Namespace Identifier Used3	Command
(07)	(06:02)	(06:02)
Generic / Command	Function	Data Transfer4
0b	000 00b	00b	00h	M	No	Delete I/O Submission Queue
…	…	…	…	…	…	…
0b	001 01b	01b	15h	O	Yes	Namespace Attachment
0b	?	11b	16h	O	No	Set Doorbell/EventIdx Memory
I/O Command Set Specific
1b	Na	Na	80h – BFh	O		I/O Command Set specific
Vendor Specific
1b	Na	Na	C0h – FFh	O		Vendor specific
NOTES: / 1. O/M definition: O = Optional, M = Mandatory. / 2. Opcodes not listed are reserved. / 3. A subset of commands uses the Namespace Identifier field (CDW1.NSID). When not used, the field shall be / cleared to 0h. / 4. 00b = no data transfer; 01b = host to controller; 10b = controller to host; 11b = bidirectional

* Add a sub-section in 5 Admin Command Set as shown below:

5.18 Set Doorbell/EventIdx memory
The Set Doorbell/Eventidx memory command is used to reduce the number of MMIO writes to the doorbell registers by “remapping” the registers in a buffer in the host, which can improve performances mainly in virtualized environments where MMIOs are costly.
The host shall provide two buffers (Doorbell memory, updated by the host, and EventIdx memory, updated by the controller) which mimic the doorbell structure defined in section 3.1 and indicated in Figure (5.18.Figure1).
The host should update the doorbell memory instead of updating the doorbell registers as usual, if the value written in memory pass the eventIdx which refers to the same Submission/Completion Queue, then the doorbell register should be updated.

The host shall provide a memory as indicated in (5.18.Figure1) with enough size according to the parameter y given, all queue with QID greater then y will not be affected and shall use the classic doorbell registers.

The controller might read from the Doorbell memory buffer and update the EventIdx buffer before the host writes to the Doorbell register, it is implementation specific when the controller perform those actions.
The Set Doorbell/EventIdx memory command is not retained if a controller reset occurs.

Note: The consumer and producer shall take queue wrap conditions into account.
Figure (5.18.Figure1) Doorbell/EventIdx Memory buffer structure
Start (Offset in the buffer)	End (Offset in the buffer)	Description
00h	03h	Submission Queue 0 Tail Mem Doorbell or EventIdx (Admin)
00h + (1 * / (4 << CAP.DSTRD))	03h + (1 * / (4 << CAP.DSTRD))	Completion Queue 0 Head Mem Doorbell or EventIdx (Admin)
00h + (2 * / (4 << CAP.DSTRD))	03h + (2 * / (4 << CAP.DSTRD))	Submission Queue 1 Tail Mem Doorbell or EventIdx
00h + (3 * / (4 << CAP.DSTRD))	03h + (3 * / (4 << CAP.DSTRD))	Completion Queue 1 Head Mem Doorbell or EventIdx
…	…	...
00h+ (2y * (4 << / CAP.DSTRD))	03h + (2y * (4 << / CAP.DSTRD))	Submission Queue y Tail Mem Doorbell or EventIdx
00h + / ((2y + 1) * (4 << / CAP.DSTRD))	03h + / ((2y + 1) * (4 << / CAP.DSTRD))	Completion Queue y Head Mem Doorbell or EventIdx

Figure (5.18.Figure 2): Set Doorbell/EventIdx Memory - PRP Entry 1
Bit	Description
63:00	PRP Entry 1 (PRP1): This field contains the first PRP entry, specifying the start of the Doorbell memory data buffer.

Figure (5.18.Figure 3): Set Doorbell/EventIdx Memory - PRP Entry 2
Bit	Description
63:00	PRP Entry 2 (PRP2): This field contains the second PRP entry. Refer to Figure 11 for the definition of this field.

Figure (5.18.Figure 4): Set Doorbell/EventIdx Memory - Command Dword 10 and Command Dword 11
Bit	Description
63:00	EventIdx Data Pointer (EDPTR): This field contain the equivalent PRP1 and PRP2 for the EventIdx data buffer. Command Dword 10 contain the PRP1 and Command Dword 11 the PRP2.

Figure (5.18.Figure 5): Set Doorbell/EventIdx Memory - Command Dword 12
Bit	Description
31:00	Number of queues (NQS): The y value as indicated in (5.18.Figure1) which defines the minimum size of the data buffers and the number of queues to cover. This is a 0’s based value.

5.18.1 Command Completion
If the command is completed, then the controller shall post a completion queue entry to the Admin
Completion Queue indicating the status for the command.
Set Doorbell/EventIdx memory command specific status values are defined in Figure (5.18.Figure 6).

Figure (5.18.Figure 6): Set Doorbell/EventIdx Memory – Command Specific Status Values
Value	Description
0Ch	Invalid memory address

* Add the following option in the Identify commands Figure 90

Figure 90: Identify – Identify Controller Data Structure
Bytes	O/M	Description
Controller Capabilities and Features
01:00	M	PCI Vendor ID (VID): Contains the company vendor identifier that is assigned by / the PCI SIG. This is the same value as reported in the ID register in section 2.1.1.
...	...	...
Admin Command Set Attributes & Optional Controller Capabilities
257:256	M	Optional Admin Command Support (OACS): This field indicates the optional / Admin commands supported by the controller. Refer to section 5. / Bits 15:5 are reserved. / Bit 4 if set to '1' then the controller supports the Set Doorbell/EventIdx Memory command. If cleared to '0' then the controller does not support the Set Doorbell/EventIdx Memory command. / Bit 3 if set to ‘1’ then the controller supports the Namespace Management and / Namespace Attachment commands. If cleared to ‘0’ then the controller does not / support the Namespace Management and Namespace Attachment commands. / Bit 2 if set to ‘1’ then the controller supports the Firmware Commit and Firmware / Image Download commands. If cleared to ‘0’ then the controller does not support / the Firmware Commit and Firmware Image Download commands. / Bit 1 if set to ‘1’ then the controller supports the Format NVM command. If cleared / to ‘0’ then the controller does not support the Format NVM command. / Bit 0 if set to ‘1’ then the controller supports the Security Send and Security Receive / commands. If cleared to ‘0’ then the controller does not support the Security Send / and Security Receive commands.
…	…	...